## Slide 1
RSM & EGO

## Slide 2: Contexte
Nouvelles configurations
Pas de modèle semi-empirique
Optimisation Globale
Utilisation de codes couteux en temps (dés l’avant projet)
Modèles de substitution

## Slide 3: Plan d’expérience
Information sur la fonction dans un espace de design
Echantillonnage de points suivant plusieurs méthodes
LHS
Grille régulière
Hasard

## Slide 4: Modèle de substitution
Utilisation des points échantillonnés pour trouver une fonction de prédiction
Régression Linéaire
Régression Quadratique
Processus Gaussien
Donne une prédiction pour chaque point du domaine
et une erreur globale
Donne une prédiction et une erreur pour chaque point du domaine

## Slide 5: Comment savoir si le modèle est bon
Coefficient de détermination
Erreur quadratique moyenne
Erreur médiane absolue
sont les points de la base de test
sont les valeurs réelles de la fonctions
sont les valeurs prédites
est le nombre de points dans la base de test
Les points de la base de test sont différents des points de la base d’apprentissage

## Slide 6: Optimisation par modèle de substitution
Plan d’expérience
Entrainement du modèle de substitution
Evaluer les points
Optimization problem

## Slide 7: Retour sur les GP
Rasmussen, C. E. and Williams, C. K. I. Gaussian Processes for Machine Learning. The MIT Press, 2006.
Processus Gaussien (GP) (Rasmussen et al., 2006)
 Prediction du modèle GP
 Exploitation de l’information
 Incertitude du modèle GP
 Exploration du domaine de conception
Il faut utiliser ces informations simultanément !!! Exploration vs Exploitation

## Slide 8: Les fonctions d’acquisition
Fonctions d’acquisition (Mockus et al.)
Compromis exploration/exploitation
Sous-problème d’enrichissement
(2)
Bartoli, N., Lefebvre, T., Dubreuil, S., Olivanti, R., Priem, R., Bons, N., Martins, J. R. A. A., Morlier, J. Adaptive modeling strategy for constrained global optimization with application to aerodynamic wing design. Aerospace Science and Technology, 90:85–102, 2019.
Hernández-Lobato, D., Hernandez-Lobato, J., Shah, A., & Adams, R. Predictive entropy search for multi-objective bayesian optimization. In International Conference on Machine Learning, pp. 1492–1501, 2016.
Mockus, J. On Bayesian methods for seeking the extremum. In Optimization Techniques IFIP Technical Conference, pp. 400–404, 1975.
Picheny, V., Gramacy, R. B.,Wild, S., and Le Digabel, S. Bayesian optimization under mixed constraints with a slack-variable Augmented Lagrangian. In Advances in Neural Information Processing Systems 29, pp. 1435–1443, 2016.
Picheny, V. A stepwise uncertainty reduction approach to constrained global optimization. In Artificial Intelligence and Statistics, pp. 787–795, 2014.
Srinivas, N., Krause, A., Kakade, S. M., and Seeger, M. Gaussian process optimization in the bandit setting: No regret and experimental design. In 27th International Conference on Machine Learning (ICML-10), pp. 1015–1022, 2010.
Wang, Z., Jegelka, S. Max-value entropy search for efficient Bayesian optimization. In Proceedings of the 34th International Conference on Machine Learning-Volume 70. pp. 3627–3635, 2017.
Watson, A. G., Barnes, R. J. Infill sampling criteria to locate extremes. Mathematical Geology, 27:589–608, 1995.
SUR (Picheny et al)
PES (Hernadez-lobato et al.)
MES (Wang et al.)
AL (Picheny et al.)
Explicite
Implicite
EI (Mockus et al.)
UCB (Srinivas et al.)
WB2 (Watson and Barnes)
WB2S (Bartoli et al., )
Ajouter des points que dans les zones intéressantes !!!!

## Slide 9: Optimisation Bayésienne
Plan d’expériences
Entrainement du modèle Bayésien
Evaluer les points
Fonction à optimiser
Processus Gaussien
Fonction d’acquisition
Points connus
Points à ajouter

## Slide 10: Prendre les contraintes en compte
Existing enrichment concepts
(2)
2 types of sub-optimization problem
Unconstrained
Constrained
+ Gather all the information
Not adapted to highly constrained optimization problems
+ Adapted to highly constrained optimization problems
Dispersed information
Ex: (Picheny et al., 2016)
Ex: (Sasena et al.,2002 ; Audet et al., 2000 ; Priem et al., 2019)
Optimization problem
Feasibility criterion (Priem et al, 2020)
Priem, R., Bartoli, N., Diouane, Y. & Sgueglia, A. Upper trust bound feasibility criterion for mixed constrained Bayesian optimization with application to aircraft design. Aerospace Science and Technology , 105, 105980 (2020).
Audet, C., Dennis, J., Moore, D., Booker, A., & Frank, P. A surrogate-model-based method for constrained optimization. In 8th Symposium on Multidisciplinary Analysis and Optimization. pp. 4891, 2000.
Sasena, M. J., Papalambros, P., and Goovaerts, P. Exploration of metamodeling sampling criteria for constrained global optimization. Engineering optimization, 34:263–278, 2002.
Bartoli, N., Lefebvre, T., Dubreuil, S., Olivanti, R., Priem, R., Bons, N., Martins, J. R. A. A., Morlier, J. Adaptive modeling strategy for constrained global optimization with application to aerodynamic wing design. Aerospace Science and Technology, 90:85–102, 2019.
exploration/exploitation feasibility trade-off
Use of uncertainty and prediction of the constraints models
Examples:
MC
PF
EV
UTB
Different versions of UTB are available

## Slide 11: Prendre les contraintes en compte
2 design variables
1 inequality constraint
Modified Branin (MB) (Parr et al., 2010)
Parr, J., Holden, C. M. E., Forrester, A. I. J., and Keane, A. J. Review of efficient surrogate infill sampling criteria with constraint handling. In 2nd International Conference on Engineering Optimization, pp. 1–10, 2010.
Priem, R., Bartoli, N., Diouane, Y. & Sgueglia, A. Upper trust bound feasibility criterion for mixed constrained Bayesian optimization with application to aircraft design. Aerospace Science and Technology , 105, 105980 (2020).
Sasena, M. J., Papalambros, P., and Goovaerts, P. Exploration of metamodeling sampling criteria for constrained global optimization. Engineering optimization, 34:263–278, 2002.
MC (Sasena et al., 2002)
UTB (Priem et al., 2020)

## Slide 12: Exemple 1
EU H2020 project, 2015-2018
Optimization Problem
18 design variables (8 for the inlet, 10 for the nozzle)
1 objective function (thrust-minus-drag losses),
2 equality constraints for the mass flow rates
CFD computations (TsAGI in-house code EWT)
High-bypass-ratio engine (BPR = 13)
Regime: M = 0.78, H = 11 km (Cruise)
RANS, Spalart-Allmaras turb. Model
Axisymmetric grid, N = 236544 cells
1 run = 30 min on 48 cores

## Slide 13: Example 1
Optimizer settings
Initial DoE of 19 points
Constraint Tols:
Budget of 300 evals
Value
Best valid value
Priem, R., Bartoli, N. & Diouane, Y. On the Use of Upper Trust Bounds in Constrained Bayesian Optimization Infill Criteria. in Proceedings of the AIAA AVIATION 2019 FORUM 2986 (2019).

## Slide 14: Exemple 2
BRAC Baseline
Idea
Research configuration to work with universities without confidentiality constraints
Information
Based on the Challenger 300
Reist, T. A. et al. Cross Validation of Aerodynamic Shape Optimization Methodologies for Aircraft Wing-Body Optimization. AIAA Journal 1–15 (2020).
12 Variables
7 Constraints
1 run 30s on 1 proc

## Slide 15: Exemple 2
Maximum time allowed
Conclusion
SEGO is converging faster than other solvers (2h vs 8h)
SEGO-like solvers are converging faster (in time and evaluation) compared to Evol and Pointer-2
SEGO-UTB likely needs more time to converge  More explorative
Priem, R., Bartoli, N., Diouane, Y. & Sgueglia, A. Upper trust bound feasibility criterion for mixed constrained Bayesian optimization with application to aircraft design. Aerospace Science and Technology , 105, 105980 (2020).

## Slide 16: Exemple 2
Optimal Configuration
Baseline Configuration
Optimized by CMDO
Priem, R., Bartoli, N., Diouane, Y. & Sgueglia, A. Upper trust bound feasibility criterion for mixed constrained Bayesian optimization with application to aircraft design. Aerospace Science and Technology , 105, 105980 (2020).

## Slide 17: BUT du BE
Partie 1 : Optimisation des hyper-paramètres du GP
Partie 2 : Mise en place de l’algorithme EGO
Partie 3 (Optionnelle) : Mise en place de SEGO